## Slide 1: Implementation of Micro-Chip for IoT applications
Done by,
ARUMUGAM Marimuthu 60303 CHINNIAH vinodhkumar 60307 JOSEPH Jojo 60299 OKORO Oghenerume Cyril 60481 SENGUTTUVAN Dhinesh Kumar 11000 VENKATESAN Shalini- 60301

## Slide 2: OBJECTIVE
Implement and simulate a SoC using a BT connection integrated for a wireless communication with a terminal and CMOS based sensors to interact with its environment.
This SoC will implemented using the platform MicroWind for a CMOS technology of 130nm.

## Slide 3: Scale Down Benefits
120 nm Technology scale down
Gate dielectric – SiO2
Kgates – 240 mm2
Effective gate length – 70nm
Smaller
Faster
Less Power Consumption
Cheaper (If fabricates million)

## Slide 4: Microwind Software
User-friendly design tool
Simulate and design an integrated circuit at physical description level.
Innovative CMOS design tool for educational market.
It works in Lambda units (λ).
DRC Checks.
500 design rules for 130nm

## Slide 5: Very Simple Microprocessor Architecture
The goal of this project is to build a 8 bit processor at logic level
VSM Architecture includes:
1) Microinstruction 10) Bluetooth
2) Program Counter 11) Temperature Sensor
3) SRAM 12) ADC
4) Accumulator A 13) DAC
5) ALU 14) Instruction register
6) Accumulator B
7) Input register
8) Output Register

## Slide 6: VSM Architecture
VSM Architecture
Microinstruction
Clock
Clear
Program Counter
Program memory
Instruction Register
ALU
Accumulator A
Accumulator B
Input Register
Output Register
Bluetooth
Temperature sensor
ADC
DAC
Enable signal
Internal bus

## Slide 7: Enable Signal
Take the control of the bus.
Enable A – Authorize A to take control of the bus.
EnableAlu – Put the result of ALU on the bus.
EnableInstr – Put the data part of the instruction on the bus.
EnableIn – Transfer the content of external input on the bus.

## Slide 8: Four times phases
Execution of one instruction is based on four times phases.
Phase | Name | Description
Phase 1 | Address state | The content of the desired memory location is loaded into the instruction register.
Phase 2 | Increment state | The program counter address is incremented. The instruction register provides the microinstruction decoder with the instruction.
Phase 3 | Execute step 1 | Depending on the instruction, the microprocessor performs the first step of the execution phase.
Phase 4 | Execute step 2 | The microprocessor performs the second step of the execution phase.

## Slide 9: Phase 1
VSM Architecture
Microinstruction
Phase 1
Program Counter
Program memory
Instruction Register
ALU
Accumulator A
Accumulator B
Input Register
Output Register
Bluetooth
Temperature sensor
ADC
DAC
Internal bus
LoadInstr
ReadMem

## Slide 10: Phase 2
VSM Architecture
Microinstruction
Phase 2
Program Counter
Program memory
Instruction Register
ALU
Accumulator A
Accumulator B
Input Register
Output Register
Bluetooth
Temperature sensor
ADC
DAC
Internal bus
ProgCount
Feed with the instr
EnableInstr

## Slide 11: Load Instruction(LDA=00000101)
Phase 3
Microinstruction
Phase 3
Program Counter
Program memory
Instruction Register
ALU
Accumulator A
Accumulator B
Input Register
Output Register
Bluetooth
Temperature sensor
ADC
DAC
Internal bus
LoadB
EnableInstr

## Slide 12: Get Input (IN=00000100)
VSM Architecture
Microinstruction
Phase 3
Program Counter
Program memory
Instruction Register
ALU
Accumulator A
Accumulator B
Input Register
Output Register
Bluetooth
Temperature sensor
ADC
DAC
Internal bus
LoadA
EnableIn

## Slide 13: Subtraction(SUB=00000010)
Phase 4
Microinstruction
Phase 4
Program Counter
Program memory
Instruction Register
ALU
Accumulator A
Accumulator B
Input Register
Output Register
Bluetooth
Temperature sensor
ADC
DAC
Internal bus
LoadA
Sub=0
EnableAlu

## Slide 14: Give Output (OUT=00000011)
Phase 3
Microinstruction
Phase 3
Program Counter
Program memory
Instruction Register
ALU
Accumulator A
Accumulator B
Input Register
Output Register
Bluetooth
Temperature sensor
ADC
DAC
Internal bus
EnableA

## Slide 15: D-register
One of the most widely used cells in integrated circuit design.
Uses edge-triggered latches.
Information flows from input D to the Output Q only at a rise edge clock.
Circuit is based on inverters and pass transistors.
It is constructed from two memory loop circuits in series.
The cell structure includes a master memory cell(left) and slave memory cell (right).

## Slide 16: Layout of D-register

## Slide 17: Schematic Diagram

## Slide 18: Simulation result
d
clk
rst
~q
q

## Slide 19: Microinstruction
Heart of the microprocessor.
Controls the Enable and Latch signals.
Instruction code and Phase information is the input of microinstruction.
Four input AND gate used to serve as a Instruction decoder.
Stores the sequence for the last two phase for each instruction.

## Slide 20: Layout of Microinstruction

## Slide 21: Schematic Diagram

## Slide 22: Program Counter
Program Counter is a 8-bit register.
Monitor the address of the active instruction.
Counts from 00000000 to 11111111.
Counter set to 00000000 so that microprocessor starts by the first instruction.
Chain edge-sensitive D-registers.
Circuit is very simple and works Asynchronously.

## Slide 23: Schematic Diagram
Program counter

## Slide 24: Layout of Program Counter

## Slide 25: Simulation result
Clk
Cnt
Inv
Po
P1
P2
P3
P4
P5
P6
P7
Q0
Q1
Q2
Q3Q4
Q5
Q6
Q7

## Slide 26: Program Memory - SRAM
Program memory contain up to 16 bytes.
Store instructions for execution.
Each instruction coded on 8 bits.

## Slide 27: Layout of Program Memory

## Slide 28: Schematic Diagram

## Slide 29: Phase Generator
Based on edge sensitive latch and XOR gates.
It produce the four phase signals phase0 to phase3 at the negative edge of clock
Phase1 - Address state
Phase2 - Increment state
Phase3 - Execute step 1
Phase4 - Execute step 2

## Slide 30: Layout of Phase Generator

## Slide 31: Schematic Diagram

## Slide 32: Simulation Result
cnt
rst
phase0
phase1
phase2
phase3

## Slide 33: Instruction Register
Stores the content of program memory.
Gives the copy of current instruction and release the main memory.
Instruction code is stored by 8 D-register.
Data is stored by separate 8 D-register.

## Slide 34: Layout of Instruction Register

## Slide 35: Schematic Diagram

## Slide 36: Simulation Result
D0
D1
D2
D3
Db0
Db1
Db2
Db3
Db4
Db5
Db6
Db7
Ebl
B0
B1
B2
B3
B4
B5
B6
B7
Clk
Toins
..
tinst7

## Slide 37: ACCUMULATOR A
8-bit register.
Based on 8 edge-sensitive D-registers.
Build with 3 state inverter to access the internal bus.
Stores the intermediate results.
It places the accumulator results on the internal bus when Enable A signal is asserted
The register output is permanently available through AluA0…AluA7 for the operation

## Slide 38: Layout of Accumulator A

## Slide 39: Schematic Diagram

## Slide 40: Simulation Result
D0
D1
D2
D3
D4
D5
D6
D7
Ena
Alu0
.
.
Alu7
B0
B1
B2
B3
.
.
.b7
clk

## Slide 41: Arithmetic Logic Unit - ALU
Subtraction operation
Requires 8 cascaded full adder
Build two complementary things
A circuit that produces the 1’s complementary of A
A small circuit that set the initial carry to 1.

## Slide 42: Layout of ALU

## Slide 43: Schematic diagram

## Slide 44: Simulation result
A0
A1
A2
.
.
.
.
A7
B0
B1
.
.
.
B7
C
Alu0
.
.
.
.
.
Alu7

## Slide 45: Accumulator B
Similar to Accumulator A
8-bit register
Based on 8 edge-sensitive D-registers.
Mainly used to supply the numbers to execute an operation
The register output is permanently available through AluB0…AluB7 for the operation
Latch A signal used to authorize the transfer of input data.

## Slide 46: Layout of Accumulator B

## Slide 47: Schematic Diagram

## Slide 48: Simulation result
D0
D1
D2
.
.
.
.
D7
Alu0
.
.
.
.
.
Alu7
CLK
RST

## Slide 49: Input Register
8-bit register
Simple set of Eight 3-state buffers.
No need of D-registers.
Directly transfer the sensor’s data to Accumulator A.

## Slide 50: Layout of Input Register

## Slide 51: Schematic Diagram

## Slide 52: Simulation result
Data0
Data1
Data2
Data3
Data4
Data5
Data6
Data7
Enb
Out0
Out1
Out2
Out3
Out4
Out5
Out6
Out7

## Slide 53: Output Register
8-bit register.
Based on 8 D-registers cell.
Instruction performed at end of the program
Stores the output data on a fall edge of clock.
Connected to Bluetooth circuit for transfer the content of internal bus to outside terminal

## Slide 54: Layout of Output Register

## Slide 55: Schematic Diagram

## Slide 56: Simulation result
In1
In2
In3
In4
In5
In6
In7
In8
Lout
CLK
Out1
Out2
Out3
Out4
Out5
Out6
Out7
Out8

## Slide 57: ADC
8 bit ADC converts an analog value into 8 bit digital value.
Used resister ladder generates voltage reference used by voltage comparator
Open loop amplifier used as a voltage comparator.
Flash converter used for very high sampling rates.
Thermometer code into binary code.

## Slide 58: Layout of ADC

## Slide 59: Schematic diagram

## Slide 60: Simulation result
Vin
ao
a1
a2
a3
a4
a5
a6
a7
c0
c1
c2
c3.
.
.
C11

## Slide 61: DAC
Digital to Analog conversion
Used R-2R Ladder for simple and inexpensive way to perform DA conversion.
The digital data are entered through the 8 lines (D0 to D7) which is to be converted to an equivalent analog voltage (Vout) by the mean of the R/2R resistor network.

## Slide 62: Layout of DAC

## Slide 63: Schematic Diagram

## Slide 64: Simulation result
Do
D1
D2
D3
D4
D5
D6
D7
Vbias
Vbias
R-2R
Vout

## Slide 65: Temperature Sensor
PN Diode serves as a temperature sensor.
Diode voltage serves as a measuring of the temperature.
pMOS device serves as a load
-40 °C to 120 °C with a step of 20 °C.

## Slide 66: Layout of Temperature sensor

## Slide 67: Schematic Diagram

## Slide 68: Simulation result

## Slide 69: Temperature Analysis

## Slide 70: Data Array Final value Vref added to the data array. Vref decreases linearly with temperature with Slope of around –1.2 mV/°C.

## Slide 71: Radio Frequency - Bluetooth
Frequency – 2.4 GHz.
Data rate – 0.72 - 10Mb/s
Output power – 100mW

## Slide 72: Block Diagram
Radio Frequency
Voltage Controlled Oscillator
Power Amplifier

## Slide 73: Layout of Radio frequency circuit

## Slide 74: Simulation result

## Slide 75: References:
http://srv-wwwperso.insa-toulouse.fr/~sicard/microwind/students.html

## Slide 76: THANKS TO OUR PROFESSOR
Dr.Lionel Trojman, PhD

## Slide 77: Thanks to our guide

## Slide 78: THANK YOU